## Slide 1
Urban Form and
Building Energy
Dr Vicky Cheng
Research Associate
Department of Architecture
Sao Paulo International Symposium 18-19 June 2012
Regional Visions of Integrated Sustainable Infrastructure Optimised for Neighbourhoods
ReVISIONS

## Slide 2
In this presentation…
Development of Generic Tiles
Generic Tiles and Energy Demand
Energy Demand Modelling for Chelmsford

## Slide 3
Linking Regional Planning to Neighbourhood Design
High level Planning:
Growths (population, economic, etc.)
Spatial development pattern
Land Use and Transport
Employment and Households
Local Decisions:
Urban Form
Infrastructural Design
(energy, water, waste, etc.)

## Slide 4
Integration of Infrastructural Design at Local Scale
Energy
Water
Waste
Local Impacts:
Economy
Environment
Health

## Slide 5
Neighbourhood Scale: Wards
London: 628 Wards
Urban
Suburban
Rural
Central
Size of Wards (households) |  | 
Central | Urban | Suburban
5219 | 4513 | 4729
Area Type Classification

## Slide 6
From City Region to Neighbourhood: Generic Tiles Method

## Slide 7
Parameters:
Built Form
Density
Land Use
Road
Garden
Building
Plot Area
Ordnance Survey Master Map
Generalized Land Use Database (GLUD)
English House Condition Survey (EHCS)
Source of data:
Generic Tiles for Domestic Buildings

## Slide 8
Terraced
Flat
(purpose-built)
Flat
(converted)
Detached
Semi-detached

## Slide 9
Terraced
Flat
(purpose-built)
Flat
(converted)
Detached
Semi-detached

## Slide 10
7
Gross Density (dwelling per hectare)
374
Detached
Flat (converted)
77
109
162
42
22
13
Semi-detached
Terraced
Flat
(purpose-built)
30
330
Da
Dd
Sa
Sd
Ta
Td
Fa
Fe
FCa
FCc
Domestic Tiles

## Slide 11
Domestic Tile Dataset
Tile Sd: Semi-detached
Gross Density (dph) | 41.7 | 
Net Density (dph) | 60.0 | 
Floor area (m2) | 85 | 
Building height (m) | 6 (2 storeys) | 
Land Use (%) | Domestic building Domestic garden Greenspace Road and path Other land | 20.04 49.68 0 30.28 0
Domestic energy demand (kWh/year/dwelling) | Space heating Water heating Cooking – gas Cooling – electricity Electrical appliances Lighting Total | 8780 1846 627 385 2036 506 14180

## Slide 12
Non-domestic Tiles
Building Footprint
Building Floorspace
Floorspace: Footprint Ratio = 2
Built Area
Plot Ratio:
Building Floorspace
Built Area
Materials provided by Peter Armitage
Building Types:
Retail
Offices
Factories
Warehouses
Non-bulk

## Slide 13
Non-domestic Tiles
Materials provided by Peter Armitage
Retail (5 Types)
Offices (5 Types)
Factories (3 Types)
Warehouses (4 Types)

## Slide 14
Non-domestic Tile Examples
Materials provided by Peter Armitage
Retail – Tile 2
(Plot Ratio = 0.6)

## Slide 15
Non-domestic Tile Examples
Materials provided by Peter Armitage
Offices – Tile 5
(Plot Ratio = 4.5)

## Slide 16
Non-domestic Tile Examples
Materials provided by Peter Armitage
Factories – Tile 1
(Plot Ratio = 0.4)

## Slide 17
Non-domestic Tiles
Further Work
1. Generic Tiles
Sub-types: Retail Warehouses, Business Parks, Department Stores, Shopping Malls
Adding Road and Green Space to Tiles
Non-domestic Building Energy Demand
Energy model has been built based on the UK Government standard SBEM (Simplified Building Energy Model)
Further develop the energy model and produce outputs for energy supply partner

## Slide 18
In this presentation…
Development of Generic Tiles
Generic Tiles and Energy Demand
Energy Demand Modelling for Chelmsford

## Slide 19
Domestic Building Energy Model Framework
Domestic Building Stock
Building Physics Model
Dwelling energy
Occupancy
Building Fabric
Services Systems
Generic Tile Data
Study Area
Dwelling Number
Dwelling Type
Location
Modelled Energy Use
Study Area
National Statistics
INPUT
PROJECTION
EVALUATE
LAND USE MODEL

## Slide 20
Domestic Building Energy Model Evaluation
Gas rs=0.934
Electricity rs=0.974
Local Authority (LA)
[326 LAs in England]
Data:
DECC Gas and electricity consumption 2007

## Slide 21
Heat and Electricity Demands by Tile Types
Month | Detached |  |  |  | Semi-detached |  |  |  | Terraces |  |  |  | Flat: purpose-built |  |  |  |  | Flat: coverted |  | 
 | Da | Db | Dc | Dd | Sa | Sb | Sc | Sd | Ta | Tb | Tc | Td | Fa | Fb | Fc | Fd | Fe | FCa | FCb | FCc
Annual | 27089 | 19019 | 13855 | 10994 | 18722 | 14573 | 12983 | 11549 | 13383 | 11739 | 11626 | 11807 | 9042 | 7224 | 6538 | 6813 | 7129 | 11823 | 9592 | 7653
1 | 4963 | 3457 | 2472 | 1902 | 3353 | 2592 | 2279 | 1987 | 2325 | 1987 | 1941 | 1964 | 1490 | 1164 | 1031 | 1077 | 1145 | 2002 | 1579 | 1229
2 | 4287 | 2983 | 2130 | 1640 | 2897 | 2240 | 1967 | 1720 | 2022 | 1735 | 1698 | 1718 | 1300 | 1013 | 898 | 937 | 982 | 1755 | 1385 | 1086
3 | 3538 | 2443 | 1734 | 1350 | 2387 | 1811 | 1599 | 1408 | 1659 | 1442 | 1434 | 1459 | 1076 | 837 | 739 | 761 | 789 | 1456 | 1162 | 911
4 | 2271 | 1567 | 1118 | 890 | 1559 | 1180 | 1046 | 937 | 1112 | 984 | 987 | 1004 | 752 | 592 | 538 | 565 | 568 | 1020 | 824 | 663
5 | 1135 | 806 | 608 | 518 | 830 | 647 | 592 | 547 | 632 | 577 | 590 | 608 | 465 | 386 | 362 | 381 | 375 | 588 | 502 | 416
6 | 366 | 301 | 271 | 258 | 324 | 287 | 277 | 274 | 294 | 288 | 296 | 293 | 257 | 224 | 220 | 227 | 234 | 285 | 261 | 228
7 | 269 | 249 | 242 | 231 | 260 | 258 | 250 | 245 | 256 | 247 | 234 | 227 | 226 | 209 | 211 | 225 | 227 | 232 | 207 | 207
8 | 275 | 254 | 244 | 234 | 268 | 260 | 252 | 247 | 259 | 249 | 236 | 228 | 228 | 210 | 212 | 225 | 229 | 234 | 209 | 206
9 | 537 | 399 | 331 | 302 | 424 | 345 | 332 | 321 | 347 | 335 | 347 | 358 | 285 | 254 | 242 | 243 | 259 | 325 | 299 | 248
10 | 1550 | 1072 | 782 | 639 | 1088 | 839 | 757 | 682 | 788 | 709 | 717 | 732 | 567 | 461 | 429 | 455 | 474 | 735 | 612 | 490
11 | 3354 | 2323 | 1660 | 1289 | 2267 | 1746 | 1547 | 1359 | 1573 | 1367 | 1362 | 1398 | 1033 | 810 | 718 | 745 | 801 | 1371 | 1104 | 850
12 | 4544 | 3166 | 2264 | 1740 | 3064 | 2368 | 2086 | 1822 | 2116 | 1818 | 1785 | 1818 | 1362 | 1064 | 938 | 971 | 1047 | 1818 | 1448 | 1119
Tile Types
Month
Annual and monthly heat demand (kWh/year per dwelling)

## Slide 22
Adjustment for local characteristics at the ward level
Regression Curves

## Slide 23
Domestic Energy Demand for Future Scenarios
Generic Tiles: New Build for Future Scenarios (2030/2050)
General Specification | 
Mode of Ventilation | Mechanical Ventilation with Heat Recovery (MVHR)
Door | Number: 2 for houses and 1 for flats U-value: 0.70 W/m2K
Windows | Type: Triple glazed (Low-E, soft-coat) Frame: uPVC U-value: 0.70 W/m2K
Ground Floor | U-value: 0.10 W/m2K (Note 1)
External Wall | Type: Solid with internal insulation U-value: 0.15 W/m2K (Note 2)
Roof | U-value: 0.10 W/m2K (Note 1)
Air Permeability q50 | 1 m3/m2/hr
Thermal Bridge y-value | 0.02 W/m2K
Lighting and appliances | Electricity use: 68% (2031) / 49% (2051) relative to 2010 level
Building Standard: Code for Sustainable Homes – Level 6 (‘Zero carbon’ Home)
UK Government Proposed Targets for New Homes
Date | 2010 | 2013 | 2016
Carbon improvement as compared to Part L (BRs 2006) | 25% | 44% | Zero carbon
Equivalent energy/carbon standard in the Code | Code Level 3 | Code Level 4 | Code Level 6

## Slide 24
Tile Sd: Semi-detached
Gross Density (dph) | 41.7
Net Density (dph) | 60.0
Floor area (m2) | 85
Building height (m) | 6 (2 storeys)
Domestic Energy Demand for Future Scenarios

## Slide 25
In this presentation…
Development of Generic Tiles
Generic Tiles and Energy Demand
Energy Demand Modelling for Chelmsford

## Slide 26
Chelmsford Case Study

## Slide 27
Chelmsford: 2001 Base Year
Urban
Suburban
Rural
Population
Annual Heat Demand (kWh/capita)
5k
8k
Dwelling Density (dph) |  | 
30 | 24 | 12

## Slide 28
Chelmsford: 2031 Future Scenarios
Urban
Suburban
Rural
Population
Trend
Market Led
Compaction
2001 Base Year
Growth in dwelling numbers from 2001 (%)
0
500
50
100
150
300

## Slide 29
Chelmsford: 2031 Trend
Heat Demand per capita
(change from 2001)
-35%
-65%
Growth Pattern
Net Dwelling Density (dph) |  | 
54 | 36 | 14
(+81%) | (+48%) | (+20%)
Heat Demand per capita (kWh/year) |  | 
2738 | 2886 | 4571
(-53%) | (-51%) | (-45%)
Share of Total Heat Demand |  | 
9% | 74% | 17%
Growth in dwelling numbers from 2001 (%)
0
500
50
100
150
300
Base Year

## Slide 30
Chelmsford: 2031 Market Led
Heat Demand per capita
(change from 2001)
-35%
-65%
Growth Pattern
Growth in dwelling numbers from 2001 (%)
0
500
50
100
150
300
Net Dwelling Density (dph) |  | 
45 | 34 | 12
(+48%) | (+40%) | (+3%)
Heat Demand per capita (kWh/year) |  | 
2796 | 2793 | 5080
(-52%) | (-52%) | (-39%)
Share of Total Heat Demand |  | 
9% | 76% | 15%
Base Year

## Slide 31
Chelmsford: 2031 Compaction
Heat Demand per capita
(change from 2001)
-35%
-65%
Growth Pattern
Growth in dwelling numbers from 2001 (%)
0
500
50
100
150
300
Net Dwelling Density (dph) |  | 
97 | 35 | 14
(+224%) | (+44%) | (+15%)
Heat Demand per capita (kWh/year) |  | 
2255 | 3025 | 4566
(-61%) | (-48%) | (-45%)
Share of Total Heat Demand |  | 
13% | 70% | 17%
Base Year

## Slide 32
Chelmsford: 2031 Future Scenarios Comparison
Scenarios | Urban | Suburban | Rural
Net Dwelling Density (dph) |  |  | 
Trend | 54 | 36 | 14
Market Led | 45 | 34 | 12
Compaction | 97 | 35 | 14
Heat Demand Reduction per capita |  |  | 
Trend | -53% | -51% | -45%
Market Led | -52% | -52% | -39%
Compaction | -61% | -48% | -45%
Share of Total Heat Demand |  |  | 
Trend | 9% | 74% | 17%
Market Led | 9% | 76% | 15%
Compaction | 13% | 70% | 17%
Trend
Market
Led
Compact

## Slide 33
Modelling of the Wider South East
Urban
Suburban
Rural
Central
Area Type Classification
Heat Demand per capita:
January (kWh/month)

## Slide 34
Building Level Technologies
Tile Db: Detached House (12 dph)
Solar PV:
Electricity Supply
Ground Source Heat Pump:
Heat Supply
Image of solar PV panel extracted from Google 3D warehouse
Low Carbon Energy Supply Options

## Slide 35
Building Level Technologies
Tile Fb: Purpose-built Flat (101 dph)
Solar PV:
Electricity Supply
Solar Thermal:
Hot Water Supply
Image of solar PV panel extracted from Google 3D warehouse
Low Carbon Energy Supply Options

## Slide 36
Community Level Technologies
Communal Infrastructure
Low Carbon Energy Supply Options
Image of solar PV panel extracted from Google 3D warehouse
Supply Technology at Building Level
Supply infrastructure at Community Level
(e.g. Combined Heat and Power)

## Slide 37
Modelling of the Wider South East
Energy Supply: Emissions

## Slide 38
Low Carbon Energy Supply Options
Infrastructure for Different Sectors
Energy
Water
Transport
Waste

## Slide 39
ReVISIONS website:
http://www.regionalvisions.ac.uk
Contact Information:
Vicky Cheng (bkc25@cam.ac.uk)
Publication:
Environmental Modelling & Software
Vol. 26 (2011), pp. 1186-1198